## Slide 1: Making Sense of Sounds: Machine Listening in the Real World
Mark Plumbley
Centre for Vision, Speech and Signal Processing (CVSSP) University of Surrey
WASPAA 2017, 18 October 2017

## Slide 2: Many thanks to …
Daniele Barchiesi
Emmanouil Benetos
Olly Bones
Trevor Cox
Bill Davies
Peter Foster
David Frohlich
Dimitrios Giannoulis
Qiang Huang
Qiuqiang Kong
Christian Kroos
Sacha Krstulovic
Jason Nurse
Sid Sigtia
Iwona Sobieraj
Dan Stowell
Wenwu Wang
Yong Xu
and many others…
And thanks to funders: EPSRC, Leverhulme Trust, EU Framework 7 & H2020, Innovate UK, ...

## Slide 3: University of Surrey

## Slide 4
15,000 students
In Guildford, County of Surrey, South East England, UK
40 mins from London
Close to Heathrow & Gatwick Airports
Next to “Surrey Hills” Area of Outstanding Natural Beauty

## Slide 5: Audio Research at Surrey
Centre for Vision, Speech and Signal Processing (CVSSP)
Technologies for machine perception of audio scenes
Institute of Sound Recording (IoSR) Research into human perception of audio quality
Digital World Research Centre (DWRC) Design of digital technologies
Centre for Digital Economy (CoDE) New business models enabled by digital technology
CVSSP
Centre for Vision, Speech and Signal Processing

## Slide 6
LVA ICA 2018
14th International Conference on Latent Variable Analysis and Signal Separation
July 2-6, 2018 University of Surrey, Guildford, UK
Paper deadline: January 15, 2018
cvssp.org/events/lva-ica-2018

## Slide 7: Outline
Introduction
Data and Data Challenges
Algorithm Performance vs Computation
Adventures with Deep Learning
  Classes hierarchy
  Spatial features
  Weakly labelled data
Privacy: Are your devices listening to you?
Conclusions

## Slide 8: Introduction: Machine Listening
Sounds: events, environment, alarms, medical, …
Sound as content (e.g. music, broadcast speech)
Sound as information (e.g. monitoring, communication)
Many new directions, e.g.:
  Security (home, professional): glass break, shouts
  “Legacy IoT”: monitoring sound-emitting devices
  Assisted living: activity sounds, assistance calls
  Environmental monitoring: birds, insects, logging
  Medical sounds: heart, lungs
  Multimedia video+sound indexing, tagging

## Slide 9: Audio Event Detection
[Figure: Tuomas Virtanen]

## Slide 10: Audio Scene Classification
[Figure: Tuomas Virtanen]

## Slide 11: Application Examples: Professional Security & Connected Home
Advanced Smart Microphone - Portable wireless audio sensor: “Internet of Sensors” detect sounds and analyse audio scenes
Audio Data Exploration: Professional/home security, multimedia database indexing, industrial/environmental monitoring
Glass breaks, smoke alarms, gun shots, car alarms, baby cries, …
Collaboration with SME Audio Analytic
Funding: Innovate UK, EPSRC, Audio Analytic
Photo: Audio Analytic
Photo: Audio Analytic

## Slide 12: Application Examples: Birdsong Identification
Strong frequency modulation (FM)
Addition of FM features help species recognition
Unsupervised feature learning gives boost vs MFCCs, Mel spectra
Best audio-only system (MAP 42.9%) in LifeCLEF 2014 bird identification challenge (501 classes, 9688 items)
Press interest (including Twitter, of course!)
Led to “Warblr” App (Stowell, Wilkinson) and Bird Audio Detection challenge
With: Stowell

## Slide 13: Data and Data Challenges

## Slide 14: Why Data Challenges?
Huge potential for automatic recognition of real-world sounds
Until recently: relatively little research activity, compared to e.g. image, speech, or even music
Barrier? -> Shortage of good open datasets for research
  Data is expensive/time-consuming to collect and label
  Commercial data may be restricted, hard to compare
Public evaluation data challenges: (1) Provide open data that researchers can use (2) Encourage reproducible research (3) Attract new researchers into the field (4) Create reference points for performance comparisons

## Slide 15: Example data challenges
Some earlier evaluation challenges, e.g.:
  MIREX: Music Information Retrieval (since 2005/6)
  PASCAL CHiME: Speech Separation (since 2006)
  CHIL CLEAR: AV from meetings (2007-8)
  SiSEC: Source Separation (since 2008)
  TRECVID Multimodal Event Detection (since 2010/11)
IEEE Audio & Acoustics Sig Proc (AASP) TC support, e.g.:
  CHiME 2, REVERB, ACE, …

## Slide 16: Detection and Classification of Acoustic Scenes and Events (DCASE 2013)
Acoustic scene classification + acoustic event detection
Scene Classification:
  busy street, quiet street, supermarket/store, restaurant, office, park, bus, tube/metro, tubestation, open market
Event Detection – (a) Office Live, (b) Office Synthetic
  door knock, door slam, speech, laughter, clearing throat, coughing, drawer, printer, keyboard click, …
See: http://c4dm.eecs.qmul.ac.uk/sceneseventschallenge/
With: Giannoulis, Stowell, Benetos, Barchiesi, Rossignol, Lagrange

## Slide 17: Timeline
Apr/May 2012: Proposed/accepted by IEEE AASP TC
Jun 2012: Initial recordings; WASPAA Special Session agreed
Jul 2012: Call for participation
Summer 2012: Community discussion, recordings
Nov-Dec 2012: Check for recording quality
Dec 2012: Public release of training/development datasets
Jan 2013: Create virtual disk image, final task spec
Feb 2013: Submit EUSIPCO paper on task and baseline systems
Apr 2013: Code submission deadline
Apr-May 2013: Run code submissions, liaise with authors
May 2013: Results released privately to authors
Jun 2013: Submit WASPAA paper
Oct 2013: Public presentation and special session at WASPAA 2013
Oct 2015: Journal paper on Challenge in IEEE Trans Multimedia
  Most popular paper of TMM for 16 of last 18 months

## Slide 18: Submitted methods for scene classification …
Scene Classification Systems

## Slide 19: … and for event detection

## Slide 20: Results (Scene Classification)
Most systems > baseline, some approach human performance
MV = Majority Vote
Participants encouraged to release software (6 released)
Human
[Barchiesi, Giannoulis, Stowell, P, 2015] [Stowell, Giannoulis, Benetos, Lagrange, P, 2015]

## Slide 21: DCASE 2013 outcomes
DCASE 2013 challenge and workshop led to
follow-up discussions between the teams,
  both at WASPAA 2013 and later conferences
Recognition of interest in topic
Ideas for follow-up challenge: DCASE-2 (2016)
Search for other data sources…

## Slide 22: CHiME-Home: Domestic Audio Tagging
What about “Smart Home” applications?
Need data from home environment
Opportunity: CHiME Challenge domestic “background noise” (designed for noisy speech recognition)
Developed with partner Audio Analytic
[Figure: Tuomas Virtanen]
With: Peter Foster, Siddharth Sigtia, Sacha Krstulovic, Jon Barker
[Foster, Sigtia, Krstulovic, Barker, P, WASPAA 2015]

## Slide 23: CHiME-Home Dataset
Recordings (7 hours) from domestic home
Audio: Background noise from CHiME Challenge [Barker et al, 2013]
Annotated in 4-sec chunks by 3 labellers
Tough annotation job: 2/3 annotators agree for only 45% of chunks.
Baseline: 0.76 - 0.98 AUC (MFCC+GMM)
Designed to be part of a data challenge…
Dataset URL: http://archive.org/details/chime-home

## Slide 24: DCASE 2016: Data Challenge and Workshop
Build on and extend success of DCASE 2013
More data, more complex, closer to real applications
Four Tasks:
Task 1: Acoustic scene classification
  Audio environment, e.g. "park", "street", "office"
Task 2: Sound event detection in synthetic audio
  Office sound events, e.g. “coughing”, “door slam”
Task 3: Sound event detection in real life audio
  Events in Home (indoor) and Residential area (outdoor)
Task 4: Domestic audio tagging (CHiME-Home)
  Activity in the home, e.g. “child speech”, “TV/Video”
With: Annamaria Mesaros, Toni Heittola, Tuomas Virtanen,
Emmanouil Benetos, Peter Foster, Mathieu Lagrange

## Slide 25: DCASE 2016: A Team Effort
International organizing team:
  Tampere University of Technology (FI)
  Queen Mary University of London (UK)
  IRCCYN (FR)
  University of Surrey (UK)
DCASE 2016 Workshop
  Satellite workshop to EUSIPCO, Budapest, Sep 2016
  23 Papers submitted to workshop

## Slide 26: DCASE 2016: Timeline & Submissions
[Mesaros, Heittola, Benetos, Foster, Lagrange, Virtanen, P, 2017]

## Slide 27: Some Issues: Data Class Imbalance
In Residential Area task:
Can get good performance by only recognizing “Bird Singing” and “Car Passing By” classes
Challenge: How to evaluate with unbalanced datasets?

## Slide 28: More recent datasets and challenges
Audio Set
From YouTube videos: 1,789,621 x 10-sec segments
Labelled with 632 audio event categories (hierarchical)
C.f. ImageNet for images, Million Song Dataset for music
DCASE 2017 Workshop: 16-17 Nov 2017, Munich, Germany
Task 1: Acoustic scene classification
Task 2: Detection of rare sound events
Task 3: Sound event detection in real-life audio
Task 4: Large-scale weakly supervised sound event detection for smart cars
http://www.cs.tut.fi/sgn/arg/dcase2017/

## Slide 30: Algorithm Performance vs Computation Cost

## Slide 31: Sound recognition in the Internet of Things
IoT – Small devices, limited computation / memory
Signal Processing “on the edge”
Best Performance vs Computational Cost?
Gaussian Mixture Models?
Support Vector Machines?
Deep Neural Network?
Explore on example audio event datasets:
Baby Cry
Smoke Alarm
Use: Mel-frequency cepstral coefficient (MFCC) features
Train on 2000 examples in each dataset
With: Siddharth Sigtia, Adam Stark, Sacha Krstulovic

## Slide 32: Performance: Detection Error Tradeoff (DET)
Baby Cry
Smoke Alarm
EER = Equal Error Rate

## Slide 33: Computational Cost? Operations per Frame
feature vector dimension
no. of Gaussian mixtures for GMM
no. of support vectors for SVM
degree of a polynomial kernel
no. of hidden units in each layer
no. of layers
(NB: Costs are for operation, not training)

## Slide 34: Performance vs number of operations
GMMs give reasonable low-cost baseline
SVMs similar performance to GMM, but more costly
DNNs very promising (deeper give better performance)
ReLU DNNs similar to sigmoid, simpler hardware (no LUT)
Baby Cry
Smoke Alarm

## Slide 35: Adventures with Deep Neural Networks

## Slide 36: Pyramid Deep Learning structure
With: Xu, Huang, Kong, Wang, Foster, Sigtia, Jackson
Task: CHiME-Home (Domestic audio tagging)

## Slide 37: Asymmetric Deep Audio Encoder (asyDAE)
Trained to reconstruct middle frame only, not entire input
Dropout used (examples indicated by “x”)
[Xu, Huang, Wang, Foster, Sigtia, Jackson, P, T-ASLP, 2017]

## Slide 38: asyDAE: Reconstruction error
Symmetric Audio Encoder tends to smooth noisy regions

## Slide 39: Promising EER performance for asyDAE

## Slide 40: Using Class Hierarchy

## Slide 41: Hierachical Acoustic Scene Taxonomy
Use hierarchy to help train the DNN

## Slide 42: Hierarchical pre-training
Train on “high-level” 3-class problem first
Transfer weights of hidden layers to refined 15-class problem

## Slide 43: Also: Multi-level objective function
Augment target output with high-level classes
Equivalent task, but likely to change learning dynamics

## Slide 44: Using Spatial Features

## Slide 45: Using spatial features
Some datesets include spatial information
E.g. CHiME-Home data recorded by binaural Head-and-Torso model in domestic home
Direction of arrival can help distinguish e.g.
  Kitchen sounds (from kitchen direction)
  TV/Video sounds (from sitting room direction)

## Slide 46: Spatial Features
Spatial features investigated:
interaural phase / time difference (IPD / ITD)
interaural level diff (ILD)
interaural magnitude diff (IMD)
Fusion layer for spatial features

## Slide 47: Visualising spatial features
Spectrogram
IMD
ILD
IPD
ILD & IPD may be affected by reverberation in room
recording

## Slide 48: Effect of Interaural magnitude difference (IMD)
DCASE 2016 Audio Tagging Task - Development Set Equal Error Rate (EER) Spectrogram (Spec), Raw waveform (RAW), Mel filter bank (MFB) Result: Adding IMD improves performance
Results on

## Slide 49: Weakly Labelled Data

## Slide 50: Weakly labelled data
Weak labels - class for whole chunk
“Class X is in here somewhere”
Compare: Strong labels – class for each frame/block
“Class X is here and here”
With: Qiuqiang Kong, Yong Xu, Wenwu Wang

## Slide 51: Joint detection and classification (JDC) model
Detector: Important blocks
Classifier: Class estimate
Combine output of detector and the classifier (“weighted pooling”)
where
class , block , detector , classifier
Final class prediction
[Kong, Xu, Wang, P, ICASSP 2017]

## Slide 52: Joint Detection-Classification: Results
Mel Spectrogram
JDC Detector output
JDC Classifier output
JDC Detector-Classifier output
Compare: Back-of-Blocks model
Labels
Equal Error Rate for method: | EER (dev. data) | EER (test data)
MFCC + GMM (baseline) | 21.3% | 20.9%
Bag of blocks | 16.7% | 19.0%
JDC | 17.3% | 16.9%

## Slide 53: JDC for Bird Audio Detection
Comparable to mean pooling
Indicates frames for classifier focus of attention
[Kong, Xu, P, EUSIPCO 2017]
Classifier feature maps (before global pooling layer)
Detector output
Mel Spectrogram

## Slide 54: DCASE 2017 Audio Tagging (Task 4a)
Log mel spectrograms
+ Convolutional recurrent neural networks (CRNNs)
+ Mini-batch data balancing in
+ Attention using Gated Linear Units (GLUs)
+ Fusion of systems
DCASE 2017 Audio Tagging: -> Best F1 score

## Slide 55: Privacy: Are you devices listening to you?
With: Jason Nurse

## Slide 56: More and more devices you can talk to…
Amazon Echo (“Alexa”)
Images: CC-BY-SA-3.0 Frmorrison at English Wikipedia; CC BY-SA 4.0 Daniel.Cardenas; Apple Press Release; Microsoft product screenshot, used with permission from Microsoft.
Apple Siri
Microsoft
Cortana
Google Home (“OK Google”)
Apple HomePod

## Slide 57: Where does the data go?
“OK Google, What’s the weather?”
“OK Google, What’s the weather?”
Internet
“What’s the weather?”
“What’s the weather?”
“Who is Prime Minister?”
“What’s the time?”
“How far is London?”
“Who is Prime Minister?”
“What’s the time?”
“How far is London?”
“Who is Prime Minister?”
“What’s the time?”
“How far is London?”
30 degrees and sunny
“30 degrees
and sunny”
“What’s the weather?”
“What’s the weather?”

## Slide 58: But: It doesn’t just respond to you…
Notes: Usage issues and accidents in device usage – perfect example is of the 6 year old that ordered a £140 doll house and box of cookies from Alexa. (link: http://www.foxnews.com/tech/2017/01/03/6-year-old-accidentally-orders-high-end-treats-with-amazons-alexa.html)
Issues become more profound as tv news reports cause more Alexa devices to be activated and more doll houses purchased! (link: http://www.cbsnews.com/news/tv-news-anchors-report-accidentally-sets-off-viewers-amazons-echo-dots/)
Companies coming up with clever ways to exploit these devices presence in our homes, e.g., Burger Kings new advert (link: https://www.youtube.com/watch?v=U_O54le4__I)

## Slide 59: Other ways to misuse “my” voice assistant…
Notes: Usage issues and accidents in device usage – perfect example is of the 6 year old that ordered a £140 doll house and box of cookies from Alexa. (link: http://www.foxnews.com/tech/2017/01/03/6-year-old-accidentally-orders-high-end-treats-with-amazons-alexa.html)
Issues become more profound as tv news reports cause more Alexa devices to be activated and more doll houses purchased! (link: http://www.cbsnews.com/news/tv-news-anchors-report-accidentally-sets-off-viewers-amazons-echo-dots/)
Companies coming up with clever ways to exploit these devices presence in our homes, e.g., Burger Kings new advert (link: https://www.youtube.com/watch?v=U_O54le4__I)

## Slide 60: Privacy impact if data is shared / hacked?
Notes: Interesting case in the US where someone’s smart home is being used against them. Specifically the police have sought to get access to voice recordings from Amazon in a murder investigation (link: https://techcrunch.com/2017/03/12/alexa-privacy/)
While we hope companies will keep our data safe, what if they don’t and are hacked – CloudPets is a good example of this (link: http://www.huffingtonpost.com.au/2017/02/28/millions-of-private-messages-between-parents-and-kids-hacked-in/)

## Slide 61: Conclusions

## Slide 62: Recognizing Everyday Sounds
Birdsong
Smart Homes:
Glass break
Smoke alarms, …
Listening out for the elderly at home?
Images: Warbl app; Audio Analytic; University of Surrey; Surrey and Borders NHS Trust ‘Internet of Things’ Test Bed
Future?
Now:
Smart Cities:
Traffic sounds, …

## Slide 63: Conclusions
Need more data – data challenges can help
  This year: DCASE 2017 challenge and workshop
Computational cost may be important
Can use Deep Learning
Many issues to consider: Class structure, weak labels, …
How handle privacy & security issues?
Just published: Virtanen, Plumbley, Ellis (Eds)